## Slide 1
RoCC custom-3 accelerator interface
Gemmini ISA
From C macro to systolic array
A top-down descent through six levels of abstraction
31 25 24 20 19 15 14 12 11 7 6 0
+------------+--------+--------+------+-------+--------+
| funct7 | rs2# | rs1# |funct3| rd |custom3 |
+------------+--------+--------+------+-------+--------+
opcode 5-bit 5-bit xd/ x0 0x7B
select reg # reg # xs1/xs2
Reference configuration
DIM = 16 ADDR_LEN = 32 BANK_NUM = 4
BANK_ROWS = 4096 ACC_ROWS = 1024
elem_t = int8 acc_t = int32
acc_scale_t = float32
ucb-bar/gemmini README · gemmini-rocc-tests (dev) include/gemmini.h · ibm/rocc-software src/xcustom.h
Notes: Deck follows the source document's own top-down structure: state the whole mechanism in three sentences first, then descend one level at a time. All field layouts follow the dev branch — the master head carries a superseded CISC scheme.

## Slide 2
How to read this deck
Six levels, top to bottom
L0
Mental model
Three things, three places
L1
Encoding
R-type, funct7, funct3
L2
Operands
Addresses and packing
L3
Cost
What issue actually costs
L4
Instruction groups
config / move / execute / loop
L5
End to end
One full 16x16x16 trace
Rule of descent
Each level is a field of the level above it. Stop at any level and the picture is still correct — just coarser.
Notes: Set expectations: the audience can leave after L2 and still read Gemmini assembly. L3 onward is for people writing or modifying the compiler and library.

## Slide 3
0
Level 0 — Mental model
The whole mechanism, in three sentences
Notes: Everything in the deck is an elaboration of one of the next slide's three points.

## Slide 4
L0
§1.1 the short version
Three things, three places
1
The instruction is a 32-bit word in .text
Fetched through the I-cache like any other RISC-V instruction. Nothing special about it.
2
The operands are 64-bit values in the CPU integer register file
The instruction carries only 5-bit register NUMBERS — never the values themselves.
3
Gemmini has no architectural registers
The only Gemmini state software can name is SRAM, addressed by a 32-bit value living INSIDE one of those 64-bit registers.
The puzzle point 3 resolves
The instruction is 32 bits. The local address is also 32 bits. They seem not to fit —
they do not need to. They sit at different depths: one is a word in memory, the other
is a bit field inside a register.
Notes: Point 3 is the single most load-bearing fact in the whole ISA. Every apparent contradiction in the encoding tables dissolves once depth is separated from width.

## Slide 5
L0
§1.2 the five stages
Five stages from C to array
C macro
>
compiler
>
.text
>
regfile
>
RoCC port
>
Gemmini
Stage | What happens
C source | One macro call, e.g. gemmini_extended_mvin(...)
Compiler | Expands the macro to inline asm with two "r" operands; emits plain RV64I to compute them
.text | One 32-bit custom3 instruction naming two registers
CPU regfile | Holds the two 64-bit operand VALUES
RoCC port | Rocket reads the regfile and sends a RoCCCommand bundle of VALUES
Gemmini | Decodes funct7, slices the 64-bit operands into fields
The transition that matters
.text → regfile, where register NUMBERS become register VALUES. Everything downstream operates on values only.
Notes: Emphasise that Gemmini never sees an instruction address or a register number — Rocket has resolved both by the time the bundle arrives.

## Slide 6
L0
§1.3 zooming in — each box is a field of the box above it
One mvin, four depths
[1] custom3 instruction — 32 bits, lives in .text
+-------------+---------+---------+-----+---------+---------+
| funct7 = 2 | rs2=x13 | rs1=x12 | 011 | rd = x0 | custom3 |
+-------------+---------+---------+-----+---------+---------+
\_________________/ 5-bit register NUMBERS, not values
v Rocket decodes, then reads the regfile
[2] integer register file — the 64-bit VALUES, in the CPU
x12 = 0x0000_0000_8FF3_2100 <- rs1 bare pointer, nothing packed
x13 = 0x0010_0010_8000_0040 <- rs2 packed triple, expanded below
v
[3] x13 contents — 64 bits, built by compiler-emitted RV64I
+--------------+--------------+------------------------------+
| rows = 16 | cols = 16 | local address = 0x8000_0040 |
| [63:48] | [47:32] | [31:0] |
+--------------+--------------+------------------------------+
v
[4] local address — 32 bits, a FIELD inside x13, not a register
+------+------+------+-----------------------------------+
| acc | ovr | rd | row index 0x40 |
| [31] | [30] | [29] | [28:0] |
+------+------+------+-----------------------------------+
Read it downward
The instruction contains rs2 = x13 — a register NUMBER.
x13 holds a 64-bit VALUE.
That value decomposes into rows, cols and a 32-bit local address.
The local address itself decomposes into three flag bits plus a row index.
Note x12
It needed no packing at all, because it is already a pointer.
Why some operands are free and others are not: Level 3.
The two 32-bit things never coexist
One is a word in memory, the other is a bit field inside a register. They sit at different depths, so they never have to fit side by side.
Notes: This is the deck's centrepiece. Walk it slowly, top to bottom, once. Everything after this slide elaborates one of these four boxes.

## Slide 7
L0
§1.4 what the macro does
What the macro actually does
Every Gemmini macro bottoms out here
#define ROCC_INSTRUCTION_0_R_R(x, rs1, rs2, func7) \
{ \
asm volatile( \
".insn r " STR(CAT(CUSTOM_, x)) ", " \
STR(0x3) ", " STR(func7) ", x0, %0, %1" \
: \
: "r"(rs1), "r"(rs2)); \
}
gemmini_extended_mvin expands to
asm volatile(".insn r CUSTOM_3, 0x3, 2, x0, %0, %1"
: /* no outputs */
: "r"(dram_addr), /* -> %0 */
"r"(((uint64_t)rows << 48) |
((uint64_t)cols << 32) |
spad_addr)); /* -> %1 */
"r"(expr) is a GCC input constraint
Evaluate this C expression, place the result in some general-purpose register, and substitute that register's name here.
That one line is the whole mechanism.
.insn r <opcode>, <funct3>, <funct7>, <rd>, <rs1>, <rs2>
CUSTOM_3 0x3 2 x0 %0 %1
| | | | | |
0x7B xd=0, k_MVIN unused | +- 2nd input
xs1=1, +--------- 1st input
xs2=1
No deep magic in operand placement
%0 lands in the rs1 field and %1 in rs2 strictly by declaration order of the input constraints — the header author simply chose.
The one genuinely forced position is the config selector in rs1[1:0], because all four config instructions share funct7 = 0.
Notes: Common misconception to pre-empt: people assume rs1/rs2 assignment encodes semantics. It does not — except for the config selector.

## Slide 8
L0
§1.5 where state lives
Where Gemmini state lives
Gemmini state | Addressable how?
Configuration (dataflow, strides, scales, act) | NOT ADDRESSABLE. Latched by config_*, write-only, no readback
Loop-instruction operands (bounds, addrs, strides) | NOT ADDRESSABLE. Latched by LOOP_*_CONFIG_*
Scratchpad SRAM | By 32-bit local address — a VALUE in a CPU register, not a register number
Accumulator SRAM | Same
ROB, queues, PE registers | NOT VISIBLE to software
Rocket delivers a bundle, not an instruction
class RoCCCommand {
val inst = new RoCCInstruction
val rs1 = Bits(xLen.W) // 64-bit VALUE,
val rs2 = Bits(xLen.W) // already read
val status = new MStatus // privilege
} // ctx for TLB
Carry this into any derivative design
Gemmini's configuration state is invisible to the OS.
No architectural name → no save/restore path → a context switch with configuration live, or a DMA in flight, is a correctness hazard the architecture does not address.
Notes: The OS-invisibility point is the one architects reusing Gemmini most often discover too late. Worth flagging explicitly in any productisation discussion.

## Slide 9
L0
§1.6 why rs1 holds a virtual address
Why rs1 holds a virtual address
Mechanism
Gemmini's DMAs operate on virtual addresses.
Each has a private TLB (FrontendTLB); on a miss it falls back to a page-table walker shared with the host CPU via the RoCC ptw port.
The status field carries the MStatus captured at issue — the privilege context the TLB needs for permission checks.
Why it is pleasant to program
Userspace hands it plain malloc'd pointers.
no kernel driver
no dma-buf
no pinning
no software translation
One binary, two environments
rocket-chip's TLB passes VA through unchanged in Bare mode (satp.MODE = 0).
So the identical instruction stream runs bare-metal and under Linux — with no mode bit.
The result
No kernel driver, no pinning, no software address translation, and no separate build for bare-metal versus Linux.
A genuine design win when compared against accelerators that require pinned physical buffers and a driver round-trip.
Notes: Worth calling out when comparing against accelerators that require pinned physical buffers and a driver round-trip.

## Slide 10
1
Level 1 — Encoding
The 32-bit word
Notes: Short section. The encoding itself is unremarkable RISC-V; what matters is the funct7 map.

## Slide 11
L1
§2 instruction encoding
Instruction encoding
All Gemmini instructions are RoCC custom instructions on custom3 (XCUSTOM_ACC = 3, opcode 0x7B), standard RISC-V R-type layout.
31 25 24 20 19 15 14 12 11 7 6 0
+------------+--------+--------+------+-------+--------+
| funct7 | rs2# | rs1# |funct3| rd |custom3 |
+------------+--------+--------+------+-------+--------+
opcode 5-bit 5-bit xd/ x0 0x7B
select reg # reg # xs1/xs2
Decoupled access / execute
Instructions are queued and executed asynchronously through Gemmini's ROB. The core runs ahead while the array works.
Sole exception: k_FLUSH, which bypasses the queue.
funct3 bits [14:12] are RoCC's xd, xs1, xs2 — not a Gemmini field
funct3 | Binary | xd | Meaning | Used by
0x7 | 111 | 1 | writes rd, reads both sources | k_COUNTER only
0x3 | 011 | 0 | no rd (encoded as x0), reads both sources | everything else
Notes: Only counter_access ever writes rd, which is why it is the only instruction with a return path.

## Slide 12
L1
§8 funct7 map
The whole opcode space
CONFIG
0 k_CONFIG 4-way sub-selected via rs1[1:0]
DATA MOVEMENT
2 k_MVIN DRAM → local (convention: A)
1 k_MVIN2 DRAM → local (convention: B)
14 k_MVIN3 DRAM → local (convention: D)
3 k_MVOUT local → DRAM (C)
23 k_MVOUT_SPAD spad → spad
EXECUTE
6 k_PRELOAD load stationary operand
4 k_COMPUTE_PRELOADED vs. what was just preloaded
5 k_COMPUTE_ACCUMULATE WS: reuse wts / OS: accumulate
CISC LOOPS
8 k_LOOP_WS TRIGGER — matmul
9-13, 24, 25 (latch) bounds / addrs / strides
15 k_LOOP_CONV_WS TRIGGER — convolution
16-21 (latch) CONFIG_1 .. CONFIG_6
CONTROL
7 k_FLUSH bypasses the queue
126 k_COUNTER only instruction writing rd
22 (reserved) clock gating enable
Notes: Numbering is historical, not structural — mvin2 is funct7=1 while mvin is 2. Do not read meaning into adjacency.

## Slide 13
L1
§8 configuration sub-selector, rs1[1:0]
One opcode, four instructions
All configuration shares funct7 = 0. The sub-selector lives in rs1[1:0] — the one operand position the architecture genuinely forces.
Value | Symbol | Target
00 | CONFIG_EX | Execute pipeline
01 | CONFIG_LD | Load pipeline
10 | CONFIG_ST | Store pipeline
11 | CONFIG_BERT | I-BERT normalization (README: config_norm)
Enums
OUTPUT_STATIONARY 0 NO_ACTIVATION 0
WEIGHT_STATIONARY 1 RELU 1
IGELU 3
LAYERNORM 2 SOFTMAX 4
GARBAGE_ADDR 0xFFFFFFFF
Branch warning
The master head of gemmini-rocc-tests carries a superseded CISC scheme — k_CONFIG_CISC_EX, k_ADDR_AB, k_SIZE0, k_COMPUTE_CISC —
with no mvin2 / mvin3, no conv loop, and no CONFIG_BERT.
Everything in this deck follows the dev branch, which matches the README.
Notes: If someone in the room has read the master-branch header, this slide is why their field layouts disagree with ours.

## Slide 14
2
Level 2 — Operands
The address is the API
Notes: The densest section, and the one that pays off most. Most of Gemmini's expressive power lives in the address, not the opcode.

## Slide 15
L2
§4 local address format (32 bits) — shared by every instruction naming Gemmini-local memory
Local address format — 32 bits
31 30 29 28 0
+----+----+----+------------------------------------------+
| SP | ACC| ACC| row address |
| /AC| ovr| rd | |
+----+----+----+------------------------------------------+
Internalize this first
Memory is row-addressed: one address = one row of DIM elements (inputType in the scratchpad, accType in the accumulator).
Bit | Condition | Meaning
31 | always | 0 = scratchpad, 1 = accumulator
30 | accumulator WRITE | 0 = overwrite, 1 = accumulate onto existing
30 | scratchpad, or acc read | ignored
29 | accumulator READ | 0 = scaled-down inputType, 1 = raw accType
29 | scratchpad, or acc write | ignored
28:0 | always | Row address
Value | Meaning
0x0000_0000 | scratchpad row 0
0x8000_0000 | accumulator row 0, OVERWRITE on write
0xC000_0000 | accumulator row 0, ACCUMULATE on write
0xA000_0000 | accumulator row 0, read raw accType
0xFFFF_FFFF | GARBAGE_ADDR
Bit 29 = 1
Bypasses BOTH activation and scaling — the raw partial-sum path, used when accumulating across outer tiles in software.
Notes: Stress that accumulate-vs-overwrite is an address bit, not an opcode. Anyone coming from a conventional ISA will look for an opcode that does not exist.

## Slide 16
L2
§4 GARBAGE_ADDR is overloaded by position
GARBAGE_ADDR — one sentinel, four meanings
Used as | Effect
B or D operand of compute | inject a ZERO MATRIX
A operand | inject undefined data (don't care)
C operand of preload | SUPPRESS WRITEBACK
B operand of preload (WS) | DO NOT RELOAD WEIGHTS — reuse what is in the array
That last row is load-bearing
It is the mechanism the entire weight-stationary inner loop is built on. No opcode expresses weight reuse — only this sentinel does.
Sign-extension trap
spad_addr must be ZERO-extended into the upper 32 bits or it will corrupt the rows/cols fields.
This is why GARBAGE_ADDR is defined as ((uint32_t)(-1)) — becoming 0x0000_0000_FFFF_FFFF after promotion.
Had it been (int32_t)(-1), promotion would sign-extend to all ones and destroy both fields.
Design observation
Overloading by position keeps the opcode space small but makes the ISA context-sensitive to read.
Debugging requires knowing which operand slot you are looking at.
Notes: Gotcha #4 in the source. Anyone debugging garbage output should check the sentinel's slot before anything else.

## Slide 17
L2
§5 the four rs1 operand shapes — rs2 is almost always the packed triple
The four rs1 operand shapes
Shape A — bare 64-bit pointer, nothing packed
+--------------------------------------------------------------------+
| virtual DRAM byte address [63:0] |
+--------------------------------------------------------------------+
mvin, mvin2, mvin3, mvout, LOOP_*_CONFIG_ADDRS_* cost: 0
Shape B — packed triple, identical in layout to rs2
+----------------+----------------+----------------------------------+
| rows [63:48] | cols [47:32] | local address [31:0] |
+----------------+----------------+----------------------------------+
preload, compute_preloaded, compute_accumulated cost: ~4
Shape C — local address plus stride
+----------------------------------+---------------------------------+
| dst stride [63:32] | dst local address [31:0] |
+----------------------------------+---------------------------------+
mvout_spad cost: ~2
Shape D — dense configuration bitfield
+----------------------------------+---------------+-----------------+
| scale / constant [63:32] | stride[31:16] | flags+sel[15:0] |
+----------------------------------+---------------+-----------------+
config_ex/ld/st/norm, loop triggers cost: ~2-6
Shape A is free
Zero packing instructions — a pointer is already a 64-bit value in a register.
B, C and D all cost
All require compiler-emitted shifts and ORs. Level 3 has the per-instruction cost.
Note rs1[1:0] always holds the config selector. That position is forced.
Notes: The cost column is the bridge to Level 3. Flag it here so the next section does not feel like a detour.

## Slide 18
L2
§6-7 common rs2 packing and the complete rs1 / rs2 map
Complete rs1 / rs2 map
rs2, the common packing (ADDR_LEN = 32):
63 48 47 32 31 0
+---------------+---------------+---------------------------+
| rows | cols | local address |
+---------------+---------------+---------------------------+
rows must be <= DIM · cols may exceed DIM for mvin
Two patterns
For DMA, rs1 is external and rs2 is local — regardless of transfer direction.
For config, rs1 always holds the selector, which is why config_ld looks backwards.
Instruction | rs1 | rs2
mvin / mvin2 / mvin3 | virtual DRAM address [A] | packed triple [B]
mvout | virtual DRAM address [A] | packed triple [B]
mvout_spad | dst stride + dst local addr [C] | packed triple [B]
preload | packed: B/D [B] | packed: C [B]
compute_preloaded / _accumulated | packed: A [B] | packed: B/D [B]
config_ex | selector, dataflow, act, transposes, A_stride, acc_scale [D] | C_stride [63:48], sys_shift [31:0]
config_ld | selector, shrunk, id, pixel_repeats, block_stride, scale [D] | bare DRAM stride in bytes
config_st | selector, act, pooling block [D] | stride [31:0], acc_scale [63:32]
config_norm | selector, stat_id, flags, q_const [D] | igelu_qb [31:0], igelu_qc [63:32]
flush | [0] = skip / retry | unused (0)
LOOP_*_CONFIG_ADDRS_* | bare DRAM pointer [A] | bare DRAM pointer [A]
LOOP_* trigger | dense flags [D] | dense flags [D]
counter_access | config_reg | unused — writes rd
Notes: The bracketed letters are the shapes from the previous slide. Note config_ld is the odd one out: a bare stride in rs2, forced by the selector living in rs1.

## Slide 19
L2
§7 two patterns that make the map memorable
Two patterns that make the map memorable
For DMA — rs1 is external, rs2 is local
Regardless of transfer direction.
mvin and mvout use the SAME register roles even though data flows in opposite directions.
The register role tracks which memory space, not which way data flows.
For config — rs1 always holds the selector
In bits [1:0]. Forced, because all four config instructions share funct7 = 0 and the decoder needs the selector at a fixed offset in a fixed register.
Which is why config_ld looks backwards, with its plain stride sitting in rs2.
Notes: If the audience remembers only two things from Level 2, make it these two plus the local address format.

## Slide 20
3
Level 3 — Cost
What issuing an instruction actually costs
Notes: Short but essential. Without this section the CISC loop instructions look like gratuitous complexity.

## Slide 21
L3
§1.4 + §3.1-3.2 one macro call, and the RV64I the compiler emits for it
The generated assembly, line by line
Assuming a2 holds dram_addr and a5 holds spad_addr, with rows = cols = 16 and spad_addr = 0x8000_0040
gemmini_extended_mvin(dram_addr, spad_addr, DIM, DIM); // the C source (§1.4)
| compiler emits:
v
# dram_addr needs NO packing — it is already a 64-bit pointer in a2
lui a4, 0x100 # a4 = 0x0000_0000_0010_0000
addi a4, a4, 16 # a4 = 0x0000_0000_0010_0010 = (rows<<16)|cols
slli a4, a4, 32 # a4 = 0x0010_0010_0000_0000 fields to [63:48],[47:32]
or a4, a4, a5 # a4 = 0x0010_0010_8000_0040 | spad_addr
.insn r CUSTOM_3, 0x3, 2, x0, a2, a4
| +-- rs2 = a4 = 0x0010_0010_8000_0040 packed, cost ~4
+------ rs1 = a2 = 0x0000_0000_8FF3_2100 pointer, cost 0
Instruction | Effect here
lui rd, imm | 0x100 << 12 = 0x100000, placing cols at bit 16
addi rd, rs, imm | +16 places rows at bit 0 → 0x100010
slli rd, rs, sh | << 32 lifts both fields to [63:48], [47:32]
or rd, rs1, rs2 | merges the runtime spad_addr into [31:0]
All four are plain RV64I
No relationship to Gemmini or RoCC whatsoever.
Note the compiler's factoring: rather than two shifts it builds (rows<<16)|cols as one 32-bit constant and applies a single slli 32. With DIM both fields are compile-time constants — only the OR is data-dependent.
Notes: The macro is gemmini_extended_mvin(dram_addr, spad_addr, cols, rows) with cols = rows = DIM = 16. All four packing instructions build rs2. rs1 costs nothing. That asymmetry is the whole point of the next slide.

## Slide 22
L3
§3.2-3.3 packing cost per instruction, and the issue-rate consequence
Which side pays — and why it matters
Instruction | rs1 shape | cost | rs2 shape | cost
mvin/2/3, mvout | A — bare pointer | 0 | B — packed triple | ~4
mvout_spad | C — addr + stride | ~2 | B — packed triple | ~4
preload | B — packed triple | ~4 | B — packed triple | ~4
compute_* | B — packed triple | ~4 | B — packed triple | ~4
config_* | D — dense bitfield | ~2-6 | varies | ~1-2
LOOP_*_CONFIG_ADDRS_* | A — bare pointer | 0 | A — bare pointer | 0
The execute pair pays on BOTH operands
And it is the pair sitting in the innermost loop.
16
cycles the array is busy
for one DIM x DIM compute
8-10
host instructions
for a single compute
12-20
host instructions
for a preload + compute pair
The host is at parity with the array
Rocket is single-issue and in-order, so the core is roughly at parity with the array just ISSUING work. Any extra address arithmetic starves the accelerator.
This motivates both throughput mechanisms: decoupled access/execute, and the CISC loop instructions.
Notes: This slide explains why the CISC loop instructions exist at all, given they add no functionality. Do not skip it before Level 4.

## Slide 23
4
Level 4 — Instruction groups
Configuration · movement · execute · CISC loops · control
Notes: The longest section. If time is short, prioritise the execute pair and the WS inner loop.

## Slide 24
L4
§9.1 config_ex — selector 00
config_ex — the execute pipeline
rs1
63 32 31 16 15 10 9 8 7 6 3 2 1 0
+------------------------+--------------+---------+--+--+--+-----+--+---+
| acc_scale (float32) | A_stride | - |Bt|At|so| act |df| 00|
+------------------------+--------------+---------+--+--+--+-----+--+---+
rs2
63 48 47 0
+------------+-----------------------------------------------+
| C_stride | sys_shift |
+------------+-----------------------------------------------+
sys_shift is OS only — silently meaningless in WS
Bits | Field | Meaning
[1:0] | selector | must be 00
[2] | dataflow | 0 = OS, 1 = WS
[6:3] | sys_act | activation enum
[7] | set_only_strides | update strides without disturbing other state
[8] | A_transpose | route A through the transposer
[9] | B_transpose | route B through the transposer
[31:16] | A_stride | scratchpad row stride feeding A into the array
[63:32] | sys_acc_scale | accumulator → inputType scale (float32)
Example — WS, no activation, shift 0,
acc_scale = 1.0f, C_stride = 1, A_stride = 1
funct7 = 0
rs1 = 0x3F80_0000_0001_0004
|- 1.0f -||A_str=1||df=1(WS)<<2|sel=00|
rs2 = 0x0001_0000_0000_0000
|C_stride=1 <<48| |- sys_shift = 0 -|
Notes: set_only_strides is the escape hatch for changing stride mid-kernel without clobbering dataflow and activation.

## Slide 25
L4
§9.1 transpose × dataflow legality — from the README
Transpose × dataflow is not orthogonal
Dataflow | Transpose A | Transpose B | Permitted
OS | no | no | yes
OS | no | yes | NO
OS | yes | no | yes
OS | yes | yes | yes
WS | no | no | yes
WS | no | yes | yes
WS | yes | no | yes
WS | yes | yes | NO
Why the gaps exist
There is a single hardware transposer, and it sits on the A path.
In OS, B flows down the path that has no transposer — so OS + B-transpose only is unrepresentable.
Reading the table correctly
The legality pattern is a direct fingerprint of the datapath, not an arbitrary software restriction.
Any derivative design that adds a second transposer changes this table.
Notes: A good example of an ISA table that is unmemorable as a table and obvious as a datapath fact. Always present the datapath reason alongside.

## Slide 26
L4
§9.2 config_ld — selector 01
config_ld — the load pipeline
rs1 rs2 = DRAM stride in BYTES, full 64 bits
63 32 31 16 15 8 7 5 4 3 2 1 0
+------------------------+--------------+-----------+-----+---+--+---+
| mvin scale | block_stride | pix_repeat| - |id |sh| 01|
+------------------------+--------------+-----------+-----+---+--+---+
Bits | Field | Meaning
[1:0] | selector | must be 01
[2] | shrunk | 0 = accumulator mvins are accType, 1 = inputType
[4:3] | id | WHICH MVIN: 0 = mvin, 1 = mvin2, 2 = mvin3
[15:8] | pixel_repeats | experimental, likely to be removed
[31:16] | block_mvin_stride | private-memory stride between submatrices when cols > DIM
[63:32] | scale | multiply data during the move
Example — configure mvin (id=0) and mvin2 (id=1),
DRAM stride 64 B, scale 1.0f,
block_mvin_stride = DIM = 16, pixel_repeats = 1
funct7 = 0
id=0: rs1 = 0x3F80_0000_0010_0101 rs2 = 0x...0040
id=1: rs1 = 0x3F80_0000_0010_0109 rs2 = 0x...0040
^^
id field at [4:3]: 0 vs 1
The most common bug
Forgetting the id field reconfigures mvin when you meant mvin2. The symptom is wrong data with no error.
Notes: One scale per mvin is why the library can fuse dequantisation into the load — a reusable idea.

## Slide 27
L4
§9.3-9.4 config_st (selector 10) and config_norm (selector 11)
config_st and config_norm
config_st — the store pipeline
[1:0] selector — must be 10
[3:2] acc_act
[5:4] pool_stride — 0 DISABLES POOLING
[7:6] pool_size
[9:8] upad
[11:10] lpad
[31:24] pool_out_dim
[39:32] porows
[47:40] pocols
[55:48] orows
[63:56] ocols
rs2: [31:0] DRAM stride in bytes, [63:32] acc_scale
Pooling assumes NHWC layout and is experimental.
Example — stride 64 B, no act, acc_scale 1.0f, no pooling
rs1 = 0x0000_0000_0000_0002 (only the selector is set)
rs2 = 0x3F80_0000_0000_0040
config_norm — I-BERT normalization
Supports integer-only GELU, layernorm and softmax. Experimental.
rs1
[1:0] = 11 selector
[15:8] stat_id
[16] act_msb
[17] set_stats_id_only
[18] q_const_type
[63:32] q_const
rs2
[31:0] igelu_qb
[63:32] igelu_qc
Example — all constants zero
rs1 = 0x0000_0000_0000_0003
rs2 = 0x0000_0000_0000_0000
Notes: Both are experimental. config_st pooling in particular assumes NHWC and is rarely exercised.

## Slide 28
L4
§10 data movement
Data movement — three identical mvins
Macro | funct7 | Direction
gemmini_extended_mvin(dram, spad, cols, rows) | 2 | DRAM → local
gemmini_extended_mvin2(...) | 1 | DRAM → local
gemmini_extended_mvin3(...) | 14 | DRAM → local
gemmini_extended_mvout(dram, spad, cols, rows) | 3 | local → DRAM
gemmini_extended_mvout_spad(dst, dst_stride, src, cols, rows) | 23 | scratchpad → scratchpad
Why three of the same thing
The three mvins are functionally identical hardware.
They exist so A, B and D can each hold their own DRAM stride and scale simultaneously.
Library convention
mvin = A mvin2 = B mvin3 = D
Configure once outside the loop; never touch config_ld in the inner loop.
Notes: The one-scale-per-mvin design is why the library can fuse dequantisation into the load. Point it out — it is a reusable idea.

## Slide 29
L4
§10 worked bit-field examples — 16×16 tiles
Data movement — real operands
A @ 0x8FF32100 B @ 0x8FF33000 D @ 0x8FF35000 C @ 0x8FF34000
Scratchpad: A at row 0, B at row 0x3F00 (16384 - 256 = 16128)
mvin A -> spad 0x0000
funct7 = 2 rs1 = 0x0000_0000_8FF3_2100 rs2 = 0x0010_0010_0000_0000
|- bare pointer ----| |r16||c16||- addr=0x0 -|
mvin2 B -> spad 0x3F00
funct7 = 1 rs1 = 0x0000_0000_8FF3_3000 rs2 = 0x0010_0010_0000_3F00
mvin3 D -> accumulator row 0, overwrite
funct7 = 14 rs1 = 0x0000_0000_8FF3_5000 rs2 = 0x0010_0010_8000_0000
|bit31 = acc|
mvout C <- accumulator row 0 (scaled inputType read)
funct7 = 3 rs1 = 0x0000_0000_8FF3_4000 rs2 = 0x0010_0010_8000_0000
mvout_spad spad 0x200 -> spad 0x100, dst stride 1
funct7 = 23 rs1 = 0x0000_0001_0000_0100 rs2 = 0x0010_0010_0000_0200
|stride=1||dst=0x100| |r16||c16||src=0x200|
Same rs2 shape throughout
Every one of these packs rows, cols and the local address identically.
Only rs1 and funct7 change. The direction of the transfer is not encoded in the register roles.
Notes: Point at the identical rs2 column — it is the clearest illustration of the DMA pattern from Level 2.

## Slide 30
L4
§11 execute — preload + compute
Execute is always a pair
One RISC-V instruction cannot hold four addresses. So every matmul is split:
preload rs1 = stationary operand, rs2 = C
compute rs1 = A, rs2 = the other operand
 | preload rs1 | compute rs2
WS | B (weights) | D (bias)
OS | D (bias) | B
Macro | f7 | Behavior
gemmini_extended_preload(BD, C, ...) | 6 | Load stationary operand. Commits the cycle after the array receives it; array idles until a compute arrives.
gemmini_extended_compute_preloaded(A, BD, ...) | 4 | Compute against what was just preloaded
gemmini_extended_compute_accumulated(A, BD, ...) | 5 | WS: reuse loaded weights. OS: accumulate onto C already in the array.
Gotcha #3 — roles swap by dataflow
Getting this backwards yields plausible wrong numbers, not an error.
The likeliest source of a silently wrong result when porting OS code to WS.
Notes: Gotcha #3 in the source. Emphasise that nothing in the hardware will tell you the roles are wrong.

## Slide 31
L4
§11.1 real bit-field examples (WS)
Weight reuse is expressed entirely in address bits
preload, first i of a tile-column: load weights from spad 0x3F00, C -> acc row 0, OVERWRITE
funct7 = 6 rs1 = 0x0010_0010_0000_3F00 rs2 = 0x0010_0010_8000_0000
|r16||c16||- B = 0x3F00 -| |r16||c16||bit31, bit30=0|
preload, subsequent i: DO NOT reload weights
funct7 = 6 rs1 = 0x0010_0010_FFFF_FFFF rs2 = 0x0010_0010_8000_0000
|-GARBAGE-|
preload, k > 0: accumulate instead of overwrite
funct7 = 6 rs1 = 0x0010_0010_FFFF_FFFF rs2 = 0x0010_0010_C000_0000
|bit31|bit30|
compute_preloaded: A from spad 0x0000, no D
funct7 = 4 rs1 = 0x0010_0010_0000_0000 rs2 = 0x0010_0010_FFFF_FFFF
compute_accumulated: identical operands, different funct7
funct7 = 5 rs1 = 0x0010_0010_0000_0000 rs2 = 0x0010_0010_FFFF_FFFF
Read the three preload forms again
The only difference between them is the low 32 bits of two operands. No opcode changes.
Weight reuse and reduction accumulation are both expressed purely as address bits.
Notes: If the deck has one thesis, this slide is it: in Gemmini, the address space is the control interface.

## Slide 32
L4
§11.2 sp_tiled_matmul_ws — the real inner loop
The real WS inner loop
// sp_tiled_matmul_ws, gemmini.h
for (size_t k = 0; k < K; k++) {
for (size_t j = 0; j < J; j++) {
for (size_t i = 0; i < I; i++) { // i INNERMOST
const uint32_t A_sp_addr = a_transpose
? (A_sp_addr_start + (k*I + i)*DIM)
: (A_sp_addr_start + (i*K + k)*DIM);
const uint32_t B_sp_addr = b_transpose
? (B_sp_addr_start + (j*K + k)*DIM)
: (B_sp_addr_start + (k*J + j)*DIM);
// ... conditional mvin of A and B ...
uint32_t pre_sp_addr = i == 0 ? B_sp_addr
: GARBAGE_ADDR; (1)
uint32_t out_sp_addr = C_sp_addr;
if (k != 0)
out_sp_addr &= ~(1 << (ADDR_LEN-2)); (2)
gemmini_extended_preload(pre_sp_addr, out_sp_addr,
B_cols, B_rows, C_cols, C_rows);
if (i == 0)
gemmini_extended_compute_preloaded (A_sp_addr,
GARBAGE_ADDR, A_cols, A_rows, DIM, DIM); (3)
else
gemmini_extended_compute_accumulated(A_sp_addr,
GARBAGE_ADDR, A_cols, A_rows, DIM, DIM);
}}}
1
Weights load on the first i only
GARBAGE_ADDR thereafter means "don't reload". With i innermost, one weight tile amortizes across I A-tiles. That is weight-stationary, expressed entirely through the address sentinel.
2
ADDR_LEN-2 = 30, the accumulate bit
Set on the first k (overwrite), cleared on later k so the accumulator reduces. The library initializes C_sp_addr_start with bits 31 AND 30 set (0xC000_0000).
3
compute rs2 is always garbage in WS
D does not enter via compute. Bias is preloaded into the accumulator separately with mvin3.
Notes: Loop order is not an optimisation detail — i-innermost is what makes the dataflow weight-stationary at all. Reorder the loops and the reuse silently disappears.

## Slide 33
L4
§12.1 the CISC loop model
CISC loops — latch, latch, latch, trigger
These are not single instructions. Each is a sequence where the first N latch operands into controller registers and the last one triggers execution. The split exists purely because the operand set is far too wide for two 64-bit GPRs.
+- k_LOOP_WS_CONFIG_BOUNDS -+
|- k_LOOP_WS_CONFIG_ADDRS_AB | latch into controller
|- k_LOOP_WS_CONFIG_ADDRS_DC | registers (each commits
|- k_LOOP_WS_CONFIG_STRIDES_AB | immediately, no compute
|- k_LOOP_WS_CONFIG_STRIDES_DC -+ happens)
+- k_LOOP_WS TRIGGER - hardware generates the
full mvin / preload / compute /
mvout stream
Constraints that bite
Must be issued consecutively — no tag, no handle. Interleaving two setups corrupts both.
Half-scratchpad constraint — operands must fit in HALF the private memory, because the unroller double-buffers.
WS only. Experimental per the README.
They add no functionality — so why do they exist?
Anything they do can be done by hand with mvin / preload / compute / mvout. They exist because the hardware unroller generates a better-scheduled
stream than most hand-written tiling, and because it eliminates per-operation host packing cost — the Level 3 problem.
Notes: Tie back explicitly to Level 3. Without the issue-cost argument these look like gratuitous complexity.

## Slide 34
L4
§12.2 gemmini_loop_ws — matmul
gemmini_loop_ws — the instruction sequence
# | funct7 | rs1 | rs2
1 | 9 CONFIG_BOUNDS | [15:0] pad_I, [31:16] pad_J, [63:32] pad_K | [15:0] I, [31:16] J, [63:32] K
2 | 10 CONFIG_ADDRS_AB | A (DRAM ptr) | B (DRAM ptr)
3 | 11 CONFIG_ADDRS_DC | D (DRAM ptr) | C (DRAM ptr)
4 | 12 CONFIG_STRIDES_AB | A_stride | B_stride
5 | 13 CONFIG_STRIDES_DC | D_stride | C_stride
6 | 8 LOOP_WS | trigger flags | trigger flags
Trigger rs1 Trigger rs2
63 20 19 18 17 16 15 8 7 3 2 1 0 [0] A_transpose
+--------------+------+------+-----------+-----+--+--+--+ [1] B_transpose
| - | a_id | b_id | act | - |lD|fC|ex| [2] is_resadd
+--------------+------+------+-----------+-----+--+--+--+
[0] ex_accumulate [1] full_C (C is accType) [2] low_D (D is inputType)
Sizes in units of DIM tiles
scratchpad rows of A = I * K * DIM
scratchpad rows of B = K * J * DIM
accumulator rows of D = I * J * DIM
accumulator rows of C = I * J * DIM
6
instructions issued
64
preload/compute pairs replaced
100s
host instructions saved
Notes: The 6-vs-64 ratio is the headline number, and the honest answer to "why would a RISC-V accelerator have CISC instructions".

## Slide 35
L4
§12.2 full example — C[64×64] = A[64×64] · B[64×64], int8, no bias, no activation
gemmini_loop_ws — worked example
I = J = K = 4 tiles of 16. Row strides 64 B.
# funct7 instruction rs1 rs2
1 9 CONFIG_BOUNDS 0x0000_0000_0000_0000 0x0000_0004_0004_0004
|- pad_I/J/K = 0 -| |K=4||J=4||I=4|
2 10 CONFIG_ADDRS_AB 0x0000_0000_8FF3_2100 0x0000_0000_8FF3_3000
3 11 CONFIG_ADDRS_DC 0x0000_0000_0000_0000 0x0000_0000_8FF3_4000
4 12 CONFIG_STRIDES_AB 0x0000_0000_0000_0040 0x0000_0000_0000_0040
5 13 CONFIG_STRIDES_DC 0x0000_0000_0000_0040 0x0000_0000_0000_0040
6 8 LOOP_WS (trigger) 0x0000_0000_0000_0000 0x0000_0000_0000_0000
Six instructions replace roughly 4·4·4 = 64 preload/compute pairs plus their mvins
Several hundred host instructions saved. The _spad variant replaces steps 2-5 with k_LOOP_WS_CONFIG_SPAD_AB (24) and folds C into the trigger's rs2 upper half, for operands already resident in the scratchpad. It also carries a skips field.
Notes: Note D is a null pointer here because there is no bias; the ex_accumulate flag in the trigger is how outer software tiling hooks in.

## Slide 36
L4
§12.3 gemmini_loop_conv_ws — convolution
gemmini_loop_conv_ws — six latch, one trigger
# | f7 | rs1 | rs2
1 | 16 | batch_size, in_row_dim, in_channels, out_channels | out_row_dim, pool_out_row_dim, out_col_dim, stride, padding
2 | 17 | pool_padding, pool_stride, pool_size, pool_out_col_dim, kernel_dim | pochs, pocols, porows, batches
3 | 18 | lpad, kchs, kcols, krows | in_col_dim, plpad, dpad, upad, rpad
4 | 19 | kernel_dilation, pdpad, pupad, prpad, orows | ocols, out_stride, weight_stride, in_stride
5 | 20 | weights (DRAM ptr) | output (DRAM ptr)
6 | 21 | bias (DRAM ptr) | input (DRAM ptr)
7 | 15 | TRIGGER — flags below | TRIGGER — flags below
Trigger rs1
[0] no_bias
[1] wrot180 kernel 180 deg
[2] trans_output_1203
[3] trans_weight_1203
[4] trans_weight_0132
[5] trans_input_3120
[6] dw depthwise
[15:8] max_pixels_per_row
[17:16] b_spad_id [19:18] a_spad_id
Trigger rs2
[0] no_pool [1] downsample
[2] input_dilated [10:3] activation
The most reusable idea in the ISA
The four trans_* bits are NHWC layout permutations — this is how im2col-free convolution feeds a GEMM engine.
A hardware/compiler contract, not a convenience flag.
Notes: For anyone designing a derivative NPU, the trans_* contract is the piece worth lifting wholesale — it removes im2col from the software stack entirely.

## Slide 37
L4
§12.3 full example — 3×3 conv, stride 1, pad 1, no pooling; 1×32×32×64 NHWC in and out
gemmini_loop_conv_ws — worked example
Tile: porows = pocols = pochs = 16, krows = kcols = 3, kchs = 16,
orows = ocols = 16. All row strides 64 B. Weights @ 0x8FF40000,
input @ 0x8FF32100, bias @ 0x8FF35000, output @ 0x8FF34000.
# f7 instruction rs1 rs2
1 16 CONFIG_1 0x0040_0040_0020_0001 0x0101_0020_0020_0020
|oc||ic||ird||bs| |p||s||ocd ||pord||ord|
2 17 CONFIG_2 0x0003_0020_0000_0000 0x0001_0010_0010_0010
|kd||pocd||ps||pst,ppad| |bat||por||poc||poch|
3 18 CONFIG_3 0x0003_0003_0010_0001 0x0001_0001_0100_0020
|kr||kc||kch||lpad| |rp||up||dp||plp||icd|
4 19 CONFIG_4 0x0010_0000_0000_0001 0x0040_0040_0040_0010
|orows| ... |kdil=1| |ins||ws||outs||ocols|
5 20 CONFIG_5 0x0000_0000_8FF4_0000 0x0000_0000_8FF3_4000
|- weights --------| |- output ---------|
6 21 CONFIG_6 0x0000_0000_8FF3_5000 0x0000_0000_8FF3_2100
|- bias -----------| |- input ----------|
7 15 TRIGGER 0x0000_0000_0000_0100 0x0000_0000_0000_0001
|max_pixels_per_row=1| |no_pool = 1|
Same rules as loop_ws
Half-scratchpad constraint and outer software tiling apply identically.
Seven instructions replace an entire convolution loop nest.
Notes: Worth showing alongside slide 35 — the shape of the sequence is identical, only the operand count grows.

## Slide 38
L4
§13 control
Control — flush, counter, fence
flush — funct7 = 7
retry: rs1 = 0x0000_0000_0000_0000
skip: rs1 = 0x0000_0000_0000_0001
rs2 = 0 in both cases
rs1[0]: 1 = skip a TLB request stuck on a page fault, 0 = retry it.
Executes immediately on receipt, bypassing the instruction queue — the programmer must fence around it.
The visible surface of incomplete page-fault handling: no precise resumable trap, only skip-or-retry.
counter_access — funct7 = 126
gemmini_counter_access(rd, config_reg);
// funct3 = 0x7, the only
// instruction with xd = 1
The single Gemmini instruction with a return path to the CPU register file.
gemmini_fence()
#define gemmini_fence() \
asm volatile("fence")
Not a custom instruction — a plain RISC-V fence.
It works because Rocket stalls a fence until the RoCC accelerator deasserts busy.
Notes: flush bypassing the queue is gotcha #10 — the fence discipline around it is the programmer's responsibility.

## Slide 39
L4
§14 C API layering
C API layering — call the widest variant
Consistent widening convention: base macro, then extended, extended2, ... as fields were exposed over successive revisions. config_ld has reached extended5.
gemmini_config_ld(stride)
+- gemmini_extended_config_ld(stride, scale)
+- gemmini_extended2_config_ld(..., shrunk)
+- gemmini_extended3_config_ld(..., id)
+- gemmini_extended4_config_ld(...,
block_mvin_stride, id)
+- gemmini_extended5_config_ld(...,
pixel_repeats, id) <- emits
Narrow forms pass defaults
MVIN_SCALE_IDENTITY, ACC_SCALE_IDENTITY, DIM, false.
For anything performance-relevant, call the widest variant — the defaults silently reset fields you may have set earlier.
Above these sit ordinary C tiling functions
sp_tiled_matmul_ws sp_tiled_matmul_os tiled_matmul_auto tiled_conv_auto
Notes: The "narrow forms silently reset fields" behaviour is a real footgun — it is why library code almost always calls extended5 directly.

## Slide 40
5
Level 5 — End to end
One 16×16×16 tile, weight-stationary
Notes: Ten instructions that exercise every concept in the deck.

## Slide 41
L5
§15 complete worked trace — C = A·B + D, int8, all matrices 16×16 in DRAM
Complete worked trace — weight-stationary
# funct7 instruction rs1 rs2
-- ------ --------------------- ------------------------- -------------------------
1 0 config_ex (WS) 0x3F80_0000_0001_0004 0x0001_0000_0000_0000
2 0 config_ld id=0 (A) 0x3F80_0000_0010_0101 0x0000_0000_0000_0040
3 0 config_ld id=1 (B) 0x3F80_0000_0010_0109 0x0000_0000_0000_0040
4 0 config_st 0x0000_0000_0000_0002 0x3F80_0000_0000_0040
5 2 mvin A -> spad 0x0 0x0000_0000_8FF3_2100 0x0010_0010_0000_0000
6 1 mvin2 B -> spad 0x3F00 0x0000_0000_8FF3_3000 0x0010_0010_0000_3F00
7 14 mvin3 D -> acc 0x0 0x0000_0000_8FF3_5000 0x0010_0010_8000_0000
8 6 preload B, C=acc(acc) 0x0010_0010_0000_3F00 0x0010_0010_C000_0000
9 4 compute_preloaded A 0x0010_0010_0000_0000 0x0010_0010_FFFF_FFFF
10 3 mvout C <- acc 0x0 0x0000_0000_8FF3_4000 0x0010_0010_8000_0000
-- fence
Line 8 — why 0xC000_0000
Accumulate, because D was already moved into the accumulator at line 7.
With no bias, line 7 is dropped and line 8 uses 0x8000_0000 (overwrite).
Line 10 — why bit 29 = 0
The accumulator applies acc_scale and the activation function, delivering inputType.
Using 0xA000_0000 would return raw accType with neither applied.
Notes: Walk this line by line and point back to the level each line was introduced at. Ten instructions exercise every concept in the deck.

## Slide 42
L5
§16 gotchas
Ten gotchas
1
Instructions are not in registers.
Instructions live in .text; only operand VALUES live in the register file.
2
Config state is not context-switchable.
No save/restore path exists.
3
Operand roles swap between OS and WS.
In preload / compute.
4
GARBAGE_ADDR is overloaded.
Zero matrix, don't-care, suppress-writeback, don't-reload-weights.
5
The accumulate bit is in the address.
Not the opcode. Software toggles bit 30 of the C address.
6
Loop sequences must not be interleaved.
One latched register set.
7
sys_shift is OS-only.
Silently meaningless in WS.
8
config_ld's id field.
Forgetting it reconfigures mvin when you meant mvin2.
9
Dataflow must match elaborated hardware.
A WS-only build asked for OS produces wrong results, not an error.
10
flush bypasses the queue.
Fence yourself.
Common thread
Most failure modes are silent. Gemmini produces plausible wrong numbers far more often than it produces an error.
Notes: Close the technical content here: the ISA has almost no runtime checking, so correctness has to be enforced at the library and compiler layer.

## Slide 43
L5
Design takeaways
Four things worth carrying into a derivative design
1
The address space IS the control interface
Accumulate/overwrite, scaled/raw readback, weight reuse and writeback suppression are all address bits. Small opcode space, high expressiveness — at the cost of context-sensitive, hard-to-debug encodings.
2
Issue cost is a first-class design constraint
A single-issue in-order host is at parity with the array just ISSUING work. Decoupled access/execute and the CISC loop instructions both exist to answer this, not to add function.
3
The trans_* layout contract
Four NHWC permutation bits let a GEMM engine consume convolutions with no im2col in software. The most directly reusable idea in the ISA.
4
The unaddressed gap: OS visibility
Configuration has no architectural name, therefore no save/restore. Context switching with live config or an in-flight DMA is a correctness hazard. Page faults get skip-or-retry, not a precise resumable trap. Any productisation has to solve both.
Notes: End on the gap, not the praise — it is the part most relevant to anyone building on top of or alongside this design.

## Slide 44
Questions
Gemmini ISA — from C macro to systolic array
Sources
ucb-bar/gemmini README
ucb-bar/gemmini-rocc-tests (dev) include/gemmini.h
ibm/rocc-software src/xcustom.h
All field layouts follow the dev branch. The master head carries a superseded CISC scheme.
Notes: Close by pointing back to the branch warning — it is the single most likely source of confusion for anyone who goes to read the headers afterwards.